## Slide 1: Synthesis of OR 1200 Peripherals
Elena Weinberg
ECE 6502

## Slide 2: Introduction
Synthesized 3 OR 1200 peripherals:
Tick Timer Facility
Programmable Interrupt Controller
Power Management Unit

## Slide 3: Motivation
Power constrained age
 Power management crucial
In order to implement power-saving modes OR 1200 requires
  Power Management Unit
  Tick Timer Facility
  Programmable Interrupt Controller

## Slide 4: Overview: Tick Timer (TT)
Timer clocked by RISC clock
OS uses for precise time measurement and system scheduling
Operates from separate clock source so that doze power management mode can be implemented

## Slide 5: TT Features
Max timer count: 2^32 clock cycles
Max time period between interrupts:
2^28 clock cycles
Maskable tick timer interrupt
Single run, restartable, or continues counter modes

## Slide 6: TT implementation
TT enabled with TTMR
TTCR incremented with each clock cycle
TT Mode Register (TTMR):
-Programmed with time period
of TT and mode bits that control
operation of TT
TT Count Register (TTCR)
-Holds current value of TT
Block diagram:

## Slide 7: Timer Modes
Indicated by [M] bits in TTMR:
[TP] = Time Period, bits 27:0 of TTMR
00 | Tick timer is disabled | Disabled Timer Mode
01 | Timer is restarted when TTMR[TP] matches TTCR[27:0] | Auto-Restart Timer Mode
10 | Timer stops when TTMR[TP] matches TTCR[27:0] (change TTCR to resume counting) | One-Shot Timer Mode
11 | Timer does not stop when TTMR[TP] matches TTCR[27:0] | Continuous Timer Mode

## Slide 8: Overview: Programmable Interrupt Controller (PIC)
Receives interrupts from external sources and forwards them as low or high priority interrupt exceptions to the CPU core
PIC has 3 special-purpose registers and 32 interrupt inputs
30 other interrupt inputs can be masked and prioritized through programming special-purpose registers

## Slide 9: PIC Registers
PIC Mask Register (PICMR)
-Used to mask or unmask up to 30
programmable interrupt sources
PIC Status Register (PICSR)
-Used to determine status of each interrupt
input
PIC Priority Register (PICPR)
-Used to assign low or high priority to max of 30
interrupt sources

## Slide 10: Interrupt Handling
Peripheral asserts interrupt
Handler processes interrupt
Handler notifies peripheral that interrupt has been processed
Peripheral de-asserts interrupt
Handler clears corresponding bit in PICSR and returns
Note: peripheral must de-assert promptly

## Slide 11: PIC Implementation
Latched level-sensitive interrupt
Once interrupt line is latched (its value appears in PICSR), no new interrupts can be triggered for that line until its bit in PICSR is cleared
Block diagram:

## Slide 12: Overview: Power Management (PM)
OR 1200 has 3 power saving features:
Slow/Idle mode
Doze mode
Sleep mode

## Slide 13: Power Management Features
Slow mode  enables full functionality at lower frequency to reduce power consumption
  Usually set dynamically by OS’s idle routine that monitors usage of processor core

## Slide 14: Power Management Features
Doze mode  suspends software processing on the core by disabling all clocks to the processor internal units except to TT and PIC
  Other on-chip blocks (outside of the processor block) continue to function normally
  If interrupt occurs, processor must leave doze mode

## Slide 15: Power Management Features
  Sleep mode  all processor internal units are disabled and VDD may be lowered
  Disabled by interrupt received from PIC

## Slide 16: Power Management Register (PMR) & Implementation
32-bit special-purpose register used to enable or disable PM features & modes
  Slow Mode: Software controlled with 4-bit value in PMR[SDF]  lower value means higher performance expected from processor core
  Doze Mode: Activated by setting PMR[DME] bit
  Sleep Mode: Activated by setting PMR[SME] bit

## Slide 17: Power Management Evaluation

## Slide 18: Place and Route with IC Compiler

## Slide 19
Tick Timer
Dimensions:
45.5 X 45.5
Total area:
2071μm
Total power:
298μW

## Slide 20
PIC
Dimensions:
32.6 X 32.6
Total area:
1065μm
Total power:
157μW

## Slide 21
PM
Dimensions:
8.5 X 8.5
Total area:
72μm
Total power:
3μW

## Slide 22: Sources
The OpenRisc 1200 is an open source architecture available at
http://opencores.org/or1k/OR1200_OpenRISC_Processor

## Slide 23: Thank You!

## Slide 24: TT: DC Synthesis

## Slide 25
TT: DFT Synthesis

## Slide 26
PIC: DC Synthesis

## Slide 27
PIC: DFT Synthesis

## Slide 28: PM: DC Synthesis

## Slide 29
PM: DFT Synthesis